## Slide 1: Network-Based Denial of Service Attacks
Trends, Descriptions, and How to Protect Your Network
Craig A. Huegen <chuegen@cisco.com>
Cisco Systems, Inc.
NANOG 12 Interprovider Operations BOF
980209_dos.ppt

## Slide 2: Trends
Significant increase in network-based DoS attacks over the last year
  Attackers’ growing accessibility to networks
  Growing number of organizations connected to networks
Vulnerability
  Most networks have not implemented spoof prevention filters
  Very little protection currently implemented against attacks

## Slide 3: Profiles of Participants
Tools of the Trade
  Anonymity
  Internet Relay Chat
  Cracked super-user account on well-connected enterprise network
  Super-user account on university residence hall network
  “Throw-away” PPP dial-up accounts
Typical Victims
  IRC Users, Operators, and Servers
  Providers who eliminate troublesome users’ accounts

## Slide 4: Goals of Attacks
Prevent another user from using network connection
  “Smurf” attacks, “pepsi” (UDP floods), ping floods
Disable a host or service
  “Land”, “Teardrop”, “Bonk”, “Boink”, SYN flooding, “Ping of death”
Traffic monitoring
  Sniffing

## Slide 5: “Smurfing”
Very dangerous attack
  Network-based, fills access pipes
  Uses ICMP echo/reply packets with broadcast networks to multiply traffic
  Requires the ability to send spoofed packets
Abuses “bounce-sites” to attack victims
  Traffic multiplied by a factor of 50 to 200
  Low-bandwidth source can kill high-bandwidth connections
Similar to ping flooding, UDP flooding but more dangerous due to traffic multiplication

## Slide 6: “Smurfing” (cont’d)

## Slide 7: “Smurfing” trend
Smurf attacks are still “in style” for attackers
Significant advances made in reducing the effects
  Education campaigns through the use of white paper and other education by NOCs has reduced the average “smurf” attack from 80 Mbits/sec to 5 Mbits/sec
Most attacks can still inundate a T1 link

## Slide 8: “Land”
Goal is to severely impair or disable a host or its IP stack
Connects address and port pair to itself
Requires the ability to spoof packet source addresses
Requires the victim’s network to be unprotected against packets coming from outside with own IP addresses

## Slide 9: “Teardrop”, “Bonk”, “Boink”, “Ping of Death”
Goal is to severely impair or disable a host or its IP stack
Use packet fragmentation and reassembly vulnerabilities
Require that a host IP stack be able to receive a packet from an attacker

## Slide 10: SYN flooding
Goal is to deny access to a TCP service running on a host
Creates a number of half-open TCP connections which fill up a host’s listen queue; host stops accepting connections
Requires the TCP service be open to connections from the victim

## Slide 11: Sniffing
Goal is generally to obtain information
  Account usernames, passwords
  Source code, business critical information
Usually a program placing an Ethernet adapter into promiscuous mode and saving information for retrieval later
Hosts running the sniffer program is compromised using host attack methods

## Slide 12: Prevention Techniques
How to prevent your network from being the source of the attack:
  Apply filters to each customer network
    Allow only those packets with source addresses within the customer’s assigned netblocks to enter your network
  Apply filters to your upstreams
    Allow only those packets with source addresses within your netblocks to exit your network, to protect others
    Deny those packets with source addresses within your netblocks from coming into your network, to protect your network
This removes the possibility of your network being used as an attack source for many attacks which rely on anonymity

## Slide 13: Prevention Techniques
How to prevent being a “bounce site” in a “Smurf” attack:
  Turn off directed broadcasts to networks:
    Cisco: Interface command “no ip directed-broadcast”
    Proteon: IP protocol configuration “disable directed-broadcast”
    Bay Networks: Set a false static ARP address for bcast address
  Use access control lists (if necessary) to prevent ICMP echo requests from entering your network
  Encourage vendors to turn off replies for ICMP echos to broadcast addresses
    Host Requirements RFC-1122 Section 3.2.2.6 states “An ICMP Echo Request destined to an IP broadcast or IP multicast address MAY be silently discarded.”
    Patches are available for free UNIX-ish operating systems.

## Slide 14: Prevention Techniques
Technical help tips for Cisco routers
  BugID CSCdj35407 - “fast drop” ACL code
  BugID CSCdj35856 - ACL logging throttles
Unicast RPF checking
Interprovider Cooperation
  Stories from the field
  Publish proper procedures for getting filters put in place and tracing started

## Slide 15: References
White paper on “smurf” attacks:
  http://www.quadrunner.com/~chuegen/smurf.txt
Ingress filtering:
  ftp://ds.internic.net/internet-drafts/draft-ferguson-ingress-filtering-03.txt
MCI’s DoSTracker tool:
  http://www.security.mci.net/dostracker/
Other DoS attacks:
  “Defining Strategies to Protect Against TCP SYN Denial of Service Attacks”
    http://www.cisco.com/warp/public/707/4.html
  “Defining Strategies to Protect Against UDP Diagnostic Port Denial of Service Attacks”
    http://www.cisco.com/warp/public/707/3.html

## Slide 16: Author
  Craig Huegen
  <chuegen@cisco.com>
Questions?