## Slide 1: Distributed Denial of Service Attacks
Steven M. Bellovin
smb@research.att.com
http://www.research.att.com/~smb

## Slide 2: What Are DDoS Tools?
Clog victim’s network.
Use many sources (“daemons”) for attacking traffic.
Use “master” machines to control the daemon attackers.
At least 4 different versions in use: TFN, TFN2K, Trinoo, Stacheldraht.

## Slide 3: How They Work
Victim
Daemon
Daemon
Daemon
Daemon
Daemon
Master
Real Attacker

## Slide 4: How They Talk
Trinoo: attacker uses TCP; masters and daemons use UDP; password authentication.
TFN: attacker uses shell to invoke master; masters and daemons use ICMP ECHOREPLY.
Stacheldraht: attacker uses encrypted TCP connection to master; masters and daemons use TCP and ICMP ECHO REPLY; rcp used for auto-update.

## Slide 5: Deploying DDOS
Attackers seem to use standard, well-known holes (i.e., rpc.ttdbserver, amd, rpc.cmsd, rpc.mountd, rpc.statd).
They appear to have “auto-hack” tools – point, click, and invade.
Lesson: practice good computer hygiene.

## Slide 6: Detecting DDOS Tools
Most current IDS’s detect the current generation of tools.
They work by looking for DDOS control messages.
Naturally, these will change over time; in particular, more such messages will be properly encrypted. (A hacker PKI?)

## Slide 7: What are the Strong Defenses?
There aren’t any…

## Slide 8: What Can ISPs Do?
Deploy source address anti-spoof filters (very important!).
Turn off directed broadcasts.
Develop security relationships with neighbor ISPs.
Set up mechanism for handling customer security complaints.
Develop traffic volume monitoring techniques.

## Slide 9: Traffic Volume Monitoring
Look for too much traffic to a particular destination.
Learn to look for traffic to that destination at your border routers (access routers, peers, exchange points, etc.).
Can we automate the tools – too many queue drops on an access router will trigger source detection?

## Slide 10: Can We Do Better Some Day?
ICMP Traceback message.
Enhance newer congestion control techniques, i.e., RED.
Warning – both of these are untested ideas. The second is a research topic.

## Slide 11: ICMP Traceback
For a very few packets (about 1 in 20,000), each router will send the destination a new ICMP message indicating the previous hop for that packet.
Net traffic increase at endpoint is about .1% -- probably acceptable.
Issues: authentication, loss of traceback packets, load on routers.

## Slide 12: Enhanced Congestion Control
Define an attack as “too many packets drops on a particular access line”.
Send upstream node a message telling it to drop more packets for this destination.
Traditional RED+penalty box works on flows; this works on destination alone.
Issues: authentication, fairness, effect on legitimate traffic, implementability, etc.

## Slide 13: References
From CERT: CA-99-17, CA-2000-01, IN-99-07.
http://www.cert.org/reports/dsit_workshop.pdf
Dave Dittrich’s analyses:
  http://staff.washington.edu/dittrich/misc/trinoo.analysis
  http://staff.washington.edu/dittrich/misc/tfn.analysis
  http://staff.washington.edu/dittrich/misc/stacheldraht.analysis
Scanning tool: http://www.fbi.gov/nipc/trinoo.htm
IDS vendors, ICSA, etc.